## Slide 1: CSE231Digital Logic
Prof. Dr. Muhammad Shahin Uddin
Email: shahin.Uddin@mbstu.ac.bd

## Slide 2
Karnaugh Maps - Rules of Simplification : Summary
No zeros allowed.
No diagonals.
Only power of 2 number of cells in each group.
Groups should be as large as possible.
Every one must be in at least one group.
Overlapping allowed.
Wrap around allowed.
Fewest number of groups possible.

## Slide 3: Example 1
  Simplify F = ∑(0, 1, 2, 5, 8, 9, 10) into sum-of-products form
F(A, B, C, D)= S(0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D

## Slide 4: Example 2
Implement F(x, y, z) =
Solution to Example10
∑( 1, 2, 3, 4, 5, 7)

## Slide 5: Example 3
  F(x, y, z) = ∑(2, 3, 4, 5) = x'y + xy'
F(x, y, z) = Σ(2, 3, 4, 5) = x'y + xy'
Simplify the Boolean function F(x, y, z) = ∑(2, 3, 4, 5)

## Slide 6: Example 4
Simplify F(x, y, z) = ∑(3, 4, 6, 7)
  F(x, y, z) = ∑(3, 4, 6, 7) = yz+ xz'
F(x, y, z) = Σ(3, 4, 6, 7) = yz + xz'
F(x, y, z) =x’yz+xy’z’+xyz’+xyz
=x’yz+xz’(y’+y)+xyz
=x’yz+xz’+xyz
=yz(x’+x)+xz’
=yz+xz’

## Slide 7: Example 5
  Simplify F(x, y, z) = ∑(0, 2, 4, 5, 6)
  F(x, y, z) = ∑(0, 2, 4, 5, 6) = z'+ xy'
F(x, y, z) = Σ(0, 2, 4, 5, 6) = z' +xy'

## Slide 8: Example 6
Implement F(x, y, z) =
Solution to Example10
∑( 1, 2, 3, 4, 5, 7)

## Slide 9: Example 7
F = A'C + A'B + AB'C + BC
  Express it in sum of minterms.
  Find the minimal sum of products expression.
  F(A, B, C) = ∑(1, 2, 3, 5, 7) = C + A'B
F(A, B, C) = C + A'B

## Slide 10: Four-Variable Map
The map
  16 minterms
  Combinations of 2, 4, 8, and 16 adjacent squares
Four-variable Map

## Slide 11: Problem-08: Minimize the following boolean function- F(A, B, C, D) = Σm(0, 1, 3, 5, 7, 8, 9, 11, 13, 15)

## Slide 12: Problem-09: Minimize the following boolean function- F(A, B, C, D) = Σm(0, 1, 3, 5, 7, 8, 9, 11, 13, 15)
F(A, B, C, D) = B’C’ + D

## Slide 13: Example 10
Simplify F(w, x, y, z) = S(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
  F = y'+w'z'+xz'
F(w, x, y, z) = Σ(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14) = y' + w' z' +xz'

## Slide 14: Example11
Simplify F = ABC + BCD + A  BCD  + ABC
ABC + BCD + ABCD + ABC= BD + BC +ACD

## Slide 15: Example 12
  Simplify F = ∑(0, 1, 2, 5, 8, 9, 10) into sum-of-products form
F(A, B, C, D)= S(0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D

## Slide 16: Problem-13: Minimize the following Boolean function- F(A, B, C, D) = Σm(0, 1, 2, 5, 7, 8, 9, 10, 13, 15)

## Slide 17: Now, F(A, B, C, D) = (A’B + AB)(C’D + CD) + (A’B’ + A’B + AB + AB’)C’D + (A’B’ + AB’)(C’D’ + CD’) = BD + C’D + B’D’ Thus, minimized Boolean expression is- F(A, B, C, D) = BD + C’D + B’D’

## Slide 18: Don't-Care Conditions
The value of a function is not specified for certain combinations of variables
The don't-care conditions can be utilized in logic minimization
  Can be implemented as 0 or 1

## Slide 19: Problem-14: Minimize the following boolean function- F(A, B, C, D) = Σm(1, 3, 4, 6, 8, 9, 11, 13, 15) + Σd(0, 2, 14)

## Slide 20: Problem-14: Minimize the following boolean function- F(A, B, C, D) = Σm(1, 3, 4, 6, 8, 9, 11, 13, 15) + Σd(0, 2, 14)
F(A, B, C, D) = AD + B’D + B’C’ + A’D’

## Slide 21: Example 15
  F = yz + w'x'; F = yz + w'z
  F = ∑(0, 1, 2, 3, 7, 11, 15) ; F = ∑(1, 3, 5, 7, 11, 15)
  Either expression is acceptable
Example with don't-care Conditions
Simplify F(w, x, y, z) = ∑(1, 3, 7, 11, 15) which has the don't-care conditions d(w, x, y, z) = ∑(0, 2, 5).

## Slide 22
Karnaugh Maps – Practice
Some Selected Problems
16. Minimize the following boolean function-F(A, B, C) = Σm(1, 2, 5, 7) + Σd(0, 4, 6)
17 Minimize the following boolean function-F(A, B, C) = Σm(0, 1, 6, 7) + Σd(3, 4, 5)
18. Minimize the following boolean function-F(A, B, C, D) = Σm(0, 2, 8, 10, 14) + Σd(5, 15)
19. Consider the following boolean function- F(W, X, Y, Z) = Σm(1, 3, 4, 6, 9, 11, 12, 14)

## Slide 23: Five-Variable Map
Map for more than four variables becomes complicated
  Five-variable map: two four-variable map (one on the top of the other).
Five-variable Map

## Slide 24: Example 20
Simplify F = ∑(0, 2, 4, 6, 9, 13, 21, 23, 25, 29, 31)
F = A'B'E'+BD'E+ACE

## Slide 25: K-Map: Six-Variables
6-variable k-map is a complex k-map which can be drawn.
Visualizing 6-variable k-map is a little bit tricky.
6 variables make 64 min terms, this means that the k-map of 6 variables will have 64 cells.
Its geometry becomes difficult to draw as these cells are adjacent to each other in all direction in 3-dimensions i.e. a cell is adjacent to upper, lower, left, right, front and back cells at the same time.
we will draw it like 5-variable k-map as shown in the figure below.

## Slide 26
Solving SOP function: For clear understanding, let us solve the example of SOP function minimization of 5 Variable K-Map using the following expression
:

## Slide 27: Design Procedure
Design Procedure:
  Input: the specification of the problem
  Output : the logic circuit diagram (or Boolean function)
Step1: determine the required number of inputs and outputs from the specification
Step2: derive the truth table that defines the required relationship between inputs and outputs
Step3: obtain the simplified Boolean function for each output as a function of the input variables
Step4: draw the logic diagram and verify the correctness of the design

## Slide 28: Design of BCD to Excess -3 Code Converter Circuit
Convert from BCD code to Excess-3 code
The 6 input combinations not listed are don’t cares
These values have no meaning in BCD
We can arbitrary assign them to 1 or 0
BCD to Excess-3 Code
0 0 0 1 =1
0 0 1 1 =3
0 1 0 0 =4
+

## Slide 29: Maps for Code Conversion…. Example
The six don’t care minterms (10-15) are marked with x
z=D’
y=CD+C’D’

## Slide 30: Maps for Code Conversion…. Example
x=B’C+B’D+BC’D’
w=A+BC+BD

## Slide 31: Logic Diagram for the Converter
There are various possibilities for a logic diagram that implements a circuit
A two-level logic diagram may be obtained directly from the Boolean expressions derived by the maps
The expressions may be manipulated algebraically to use common gates for two or more outputs
Reduce the number of gates used

## Slide 32: Logic Diagram for the Converter
D’
CD
C+D
(C+D)’

## Slide 33: Design of BCD to Gray Code Converter Circuit
Convert from BCD (0-9) code to Gray code
The 6 input combinations not listed are don’t cares
We can arbitrary assign them to 1 or 0 (don’t care)
BCD to Gray Code
BCD 0 0 0 1 = Gray

## Slide 34: Application of Combinational Circuit

## Slide 35
A parity generator is a combinational logic circuit that generates the parity bit in the transmitter
On the other hand, a circuit that checks the parity in the receiver is called parity checker
Parity Generator
Parity Bit:
The parity generating technique is one of the most widely used error detection techniques for the data transmission.
In digital systems, when binary data is transmitted and processed, data may be subjected to noise so that such noise can alter 0s (of data bits) to 1s and 1s to 0s.
Hence, parity bit is added to the word containing data in order to make number of 1’s either even or odd.

## Slide 36: Parity Generation and Checking

## Slide 37: Parity Generation and Checking

## Slide 38: Even Parity Generator
K-map simplification for 3-bit message even parity generator is
From the above truth table, the simplified expression of the parity bit can be written as
0
1

## Slide 39: Even Parity Checker
The below table shows the truth table for the even parity checker :
PEC = 1 if the error occurs, i.e., the four bits received have odd number of 1s and
PEC = 0 if no error occurs, i.e., if the 4-bit message has even number of 1s.

## Slide 40: Even Parity Checker
The above logic expression for the even parity checker can be implemented by using three Ex-OR gates as shown in figure. If the received message consists of five bits, then one more Ex-OR gate is required for the even parity checking.

## Slide 41: Parity Generation and Checking
Parity Generation and Checking
  A parity bit: P = xÅyÅz
  Parity check: C = xÅyÅzÅP
    C=1: one bit error or an odd number of data bit error
    C=0: correct or an even # of data bit error
Logic Diagram of a Parity Generator and Checker

## Slide 42: Even Parity Checker
The above logic expression for the even parity checker can be implemented by using three Ex-OR gates as shown in figure. If the received message consists of five bits, then one more Ex-OR gate is required for the even parity checking.

## Slide 43: Application of Combinational Circuit

## Slide 44: Encoders
Put “Information” into code
Binary Encoder
  Example: 4-to-2 Binary Encoder
x3 x2 x1 | y1 y0
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 1 0
1 0 0 | 1 1
0
2
3
Binary Encoder
y1
y0
x0
x1
x2
x3
Only one switch should be activated at a time
1

## Slide 45: Encoders
Octal-to-Binary Encoder (8-to-3)
I7 I6 I5 I4 I3 I2 I1 I0 | Y2 Y1 Y0
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Binary Encoder
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0

## Slide 46: Decoder Circuit
A decoder is a circuit which takes an n-bits as input and use it to select (set to 1)exactly one of its 2n outputs.

## Slide 47: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
0
0
1
0
0
0
1
0
2
3
x1 | x0 | O/P
0 | 0 | 0

## Slide 48: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
0
1
0
1
0
0
1
0
2
3
x1 | x0 | O/P
0 | 0 | 0
0 | 1 | 1

## Slide 49: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
1
0
0
0
1
0
1
0
2
3
x1 | x0 | O/P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 2

## Slide 50: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
1
1
0
0
0
1
1
0
2
3
x1 | x0 | O/P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 2
1 | 1 | 3

## Slide 51: What is a Multiplexer (MUX)?
A MUX is a digital switch that has multiple inputs (sources) and a single output (destination).
The select lines determine which input is connected to the output.
MUX Types
   2-to-1 (1 select line)
   4-to-1 (2 select lines)
   8-to-1 (3 select lines)
   16-to-1 (4 select lines)
Multiplexer
Block Diagram
Select
Lines
Inputs
(sources)
Output
(destination)
1
2N
N
MUX

## Slide 52: Typical Application of a MUX
MP3 Player
Docking Station
Laptop
Sound Card
Digital
Satellite
Digital
Cable TV
Surround Sound System
MUX
D0
D1
D2
D3
Y
B | A | Selected Source
0 | 0 | MP3
0 | 1 | Laptop
1 | 0 | Satellite
1 | 1 | Cable TV
Multiple Sources
Single Destination
Selector
Notes: This slide shows a typical application of a multiplexer (in this case a 4-to-1 MUX). Have the students share other common applications of MUXs.
http://images.tigerdirect.ca/skuimages/large/Logitech-X-540-L23-7250-mai.jpg

## Slide 53: 4-to-1 Multiplexer (MUX)
B | A | Y
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
MUX
D0
D1
D2
D3
Y
B A
Notes: SSI logic diagram, block diagram, and truth table for a 4-to-1 MUX

## Slide 54: 4-to-1 Multiplexer Waveforms
D0 |  |  |  |  |  |  |  | 
D1 |  |  |  |  |  |  |  | 
D2 |  |  |  |  |  |  |  | 
D3 |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  | 
B |  |  |  |  |  |  |  | 
Y |  |  |  |  |  |  |  | 
 | D0 | D1 | D2 | D3 | D0 | D1 | D2 | D3
Input
Data
Select
Line
Output
Data
Notes: Waveform diagram for a 4-to-1 MUX. The input data signals (D0-D3) are colored RED to indicate when its is connected to the output Y. Note: There is no significance to the values of the four input data signals; they are intended solely to demonstrate that the select lines (A & B) will select what input data signal will be connected to the output.

## Slide 55
Implementation of Boolean function using multiplexer
Type #1
Let us solve some problems on implementing the Boolean expressions using a multiplexer.
In this method, 3 variables are given(say P, Q, R), which are the selection inputs for the mux.
For three selection inputs, the mux to be built was 2n = 23 = 8 : 1.
So, in this method, the type of mux can be decided by the given number of variables.
How to solve?
The first step is to select the multiplexer. If the given expression has n variables, then determine the multiplexer using the formula 2n : 1.
Connect the inputs, that correspond to the given minterms to logic 1.
Connect all the other inputs to the ground(logic 0).
Connect the input variables(P, Q, R) as the selection lines.
Solved example #1
Implement the Boolean expression F(A, B, C) = ∑ m(2, 3, 6, 7) using a multiplexer.

## Slide 56
Solution:
There are 3 variables in the given expression, hence 2n = 23 = 8 : 1 multiplexer.
So, the mux has 8 input lines, 3 selection lines, and one output.
The inputs, corresponding to the minterms (2, 3, 6, 7) are connected to the logic 1 and remaining terms to the logic 0(grounded).
The given input variables are connected as three selection lines.
Example #2
Implement the Boolean expression F(A, B, C) = ∑ m(0, 1, 3, 5, 7) using a multiplexer.
Solution:
Similar to the above problem, there are 3 variables and hence 8 : 1 multiplier is used to solve the expression.
The three input variables(A, B, C) are connected as three selection lines.
The inputs, corresponding to the minterms (0, 1, 3, 5, 7) are connected to the logic 1 and remaining terms to the logic 0(grounded).

## Slide 57
Implementation of Boolean Function in Multiplexer
Type #2
If the boolean expression has n+1 variables, we take only n variables as the selection line of the multiplexer.
The remaining single variable is used as the inputs of the mux.
In this way, any Boolean expression having n variables can be implemented with 2n-1 to 1 multiplexer.
How to solve?
From the given set of n+1 input variables, the n least significant variables are used as selection line inputs.
The 2n inputs for 2n : 1 multiplexer are derived by using an implementation table.
The implementation table has all the inputs(D0, D1, D2, D3,…) for the multiplexer, under which, all the minterms are listed in two rows.
The first row consists of all minters where A is complemented and the second row has the remaining minterms where A is in uncomplemented form.
The minterms in the given Boolean expression alone are circled.

## Slide 58
Solved example #3 (Type#2)
Implement the boolean expression F(A, B, C) = ∑ m(0, 2, 5, 6) using 4 : 1 multiplexer.
Solution:
In the given Boolean expression, there are 3 variables.
We should use 23 : 1 = 8 : 1 multiplexer. But as per the question, it is to be implemented with 4 : 1 mux.
For 4 : 1 multiplexer, there should be 2 selection lines.
So from the given 3 variables, the 2 least significant variables(B, C) are used as selection line inputs.
Look at the example of implementation table here,
Each column is analyzed separately as follows:
If both the minterms in the two rows are circled,
1 is applied to the corresponding multiplexer input.(check 4th column in the above table)
If both the minterms in the two rows are not circled, 0 is applied to the corresponding multiplexer input.(check 3rd column in the above table)
If the minterm in the first row alone is circled, is applied to the corresponding multiplexer input.(check 2nd column in the above table)
If the minterm in the second row alone is circled, is applied to the corresponding multiplexer input.(check 1st column in the above table)

## Slide 59
Let us derive the four inputs of 4 : 1 multiplexer using the implementation table.
The four inputs are listed in column-wise and all the minterms are written under the four inputs in 2 rows as shown below.
The minterms given in the boolean expression is circled and analyzed.
After analyzing, the input values of 4 : 1 mux is obtained as , A, 1, 0.
Thus the circuit can be drawn as below.

## Slide 60
Solved example #4 (Type#2)
Implement F(A, B, C, D) = ∑ m(0, 1, 5, 6, 8, 10, 12, 15) using 8 : 1 multiplexer.
Solution:
In the given boolean expression, there are 4 variables.
We should use 24 : 1 = 16 : 1 multiplexer.
But as per the question, it is to be implemented with 8 : 1 mux.
For 8 : 1 multiplexer, there should be 3 selection lines.
So from the given 4 variables, the 3 least significant variables(B, C, D) are used as selection line inputs.
From the derived input, 8 : 1 multiplexer can be drawn as below

## Slide 61
Example #5 For the given multiplexer circuit, determine the logic function.
Solution:
In the given multiplexer circuit, B and C are the selection inputs. Hence the possible input combinations are 00, 01, 10 and 11.
For these input combinations, the mux selects a particular input and gives it to the output.
That is, if BC input is 00, D0 is selected as the output. Similarly if BC = 01, D1 is selected as the output. When the input BC = 10, D2 is selected as the output. If BC = 11, D3 is selected as the output.

## Slide 62
Example 6
Implement F(A, B, C, D) = ∑ m(2, 4, 6, 7, 9, 10, 11, 12, 15) using 8: 1 multiplexer.

## Slide 63
Why Programmable Logic?
Facts:
        It is most economical to produce an IC in large volumes
  But:
  Many situations require only small volumes of ICs
  Many situations require changes to be done in the field, e.g. Firmware of a product under development
A programmable logic device can be:
  Produced in large volumes
  Programmed to implement many different low-volume designs

## Slide 64: Programmable Logic - Additional Advantages
Many programmable logic devices are field-programmable, i. e., can be programmed in the field by the user - outside of the manufacturer’s environment
Nowadays, most programmable logic devices are erasable and reprogrammable (i.e. can programmed many times)
  Allows “updating” a device or firmware, correction of errors
  Allows reuse the device for a different design - re-usability!
Concept of
Logic Programming
Locations of connections
determine the logic function implemented

## Slide 65: Hardware Programming Technologies
In the Factory - Cannot be erased/reprogrammed by user
  Mask programming (changing the VLSI mask) during manufacturing
Programmable only once
  Fuse
  Anti-fuse
Reprogrammable (Erased & Programmed many times)
  Volatile - Programming lost if chip power lost
    Single-bit storage element
  Non-Volatile - Programming survives power loss
    UV Erasable
    Electrically Erasable
      Flash (as in Flash Memory)

## Slide 66: PLDs: Basic Ideas
  A PLD consists of an array of AND gates and an array of OR gates
  Each input feeds both a non-inverting buffer and an inverting buffer to produce the true and inverted forms of each variable.
  The AND outputs are called the product lines
  Each product line is connected to one of the inputs of each OR gate
  Three fundamental types of standard PLDs: PROM, PAL, and PLA

## Slide 67: Basic Configuration of Three PLDs
(a) Programmable read-only memory (PROM)
Inputs
Fixed
AND array
(decoder)
Programmable
OR array
Outputs
Programmable
Connections
(b) Programmable array logic (PAL) device
Inputs
Programmable
AND array
Fixed
OR array
Outputs
Programmable
Connections
(c) Programmable logic array (PLA) device
Inputs
Programmable
OR array
Outputs
Programmable
Connections
Programmable
Connections
Programmable
AND array
PROM
PAL
PLA
Fixed
Connections
Fixed
Connections

## Slide 68: Wiring Conventions for Programmable Logic
We deal with a large number of gates and gate inputs
Need a more concise way of expressing gate circuits graphically
Inputs
Inputs (literals)
1 wire
X
X
A
B
A
B
Output = ?
X marks a connection, i.e. an input to the OR

## Slide 69: Read Only Memory (ROM)
Data stored in a ROM is non-volatile
Once written, this data is permanently stored until erased or changed through re-programming (if applicable)
The ROM has n input lines for the address and m output data lines
Total memory capacity of a ROM is 2n x m bits
Generally, system-level programs that need to be accessed frequently and at power up access are stored in the computer’s ROM, e.g. the BIOS firmware

## Slide 70
Compared to a ROM and a PAL, a PLA is the most flexible having a programmable set of ANDs combined with a programmable set of ORs.
Advantages
  A PLA can have large N and M permitting implementation of equations that are impractical for a ROM
  A PLA has all of its product terms connectable to all outputs, overcoming the problem of the limited inputs to the PAL ORs
  Some PLAs have outputs that can be complemented, adding POS functions
Disadvantage
  Often, the product term count limits the application of a PLA.
  Two-level multiple-output optimization reduces the number of product terms in an implementation, helping to fit it into a PLA.
Programmable Logic Array (PLA)

## Slide 71: Buffer/inverter
(a) Symbol. (b) Logic equivalent

## Slide 72
For each product term, the inputs are marked with 1, 0, or — (dash).
If a variable in the product term appears in the form in which it is true, the corresponding input variable is marked with a 1.
If it appears complemented, the corresponding input variable is marked with a 0.
If the variable is absent from the product term, it is marked with a dash.
Programmable Logic Array (PLA)

## Slide 73
PLA with three inputs, four product terms, and two outputs
Programmable Logic Array (PLA)
x exor 0=x
X exor 1=x’

## Slide 74
Example:
) (
Programmable Logic Array (PLA)

## Slide 75
Programmable Logic Array (PLA)
Implement the following Boolean function with a PLA:
Y1(A,B,C)=∑m(4, 5,7)
Y2(A,B,C)=∑m(3, 5,7)
Step 1:
A | B | C | Y1 | Y2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
Step 2: (Using K-map find minimal SOP )
Y1=AB’+AC
Y2=BC+AC
Step 3: Number of Buffer (=3)
x
x’
x
Programmable AND gate =number of function (Y1 and Y2 )=2

## Slide 76
A
B
C
Y1
Y2
Programmable Logic Array (PLA)
Y1=AB’+AC
Y2=BC+AC

## Slide 77
Programmable Logic Array (PLA)
A 3×2 PLA with 4 product terms

## Slide 78
Programmable Logic Array (PLA)
F0 = A+B' C'
F1 = A C' +A B
F2 = B' C'+A B
F3 = B' C+A
  Implement the following functions using PLA

## Slide 79
Programmable Logic Array (PLA)
  Implement the following functions using PLA
    Y1 = m(0, 1, 7)
    Y2 = m(0, 3, 6, 7)
    Y3 = m(0, 1, 3, 5, 7)

## Slide 80
Programmable Logic Array (PLA)
  Implement BCD to Gray Code Converter using PLA

## Slide 81
Programmable Logic Array (PLA)
  Implement the following functions using PLA
w(A, B, C, D) = ∑(2, 12, 13)
x(A, B, C, D) = ∑(7, 8, 9, 10, 11, 12, 13, 14, 15)
y(A, B, C, D) = ∑(0, 2, 3, 4, 5, 6, 7, 8, 10, 11, 15)
z(A, B, C, D) = ∑(1, 2, 8, 12, 13)
w = ABC’ + A’B’CD’
x = A + BCD
w = A’B + CD + B’D’
w = ABC’ + A’B’CD’ + AC’D’ + A’B’C’D = w + AC’D’ + A’B’C’D

## Slide 82
It is most commonly used type of PLD.
The PAL is a programmable logic device with a fixed OR array and a programmable AND array.
Only the AND gates are programmable, the PAL is easier to program than, but is not as flexible as, the PLA.
Figure (Next slide) shows the logic configuration of a typical PAL with four inputs and four outputs.
Programmable Array Logic (PAL)

## Slide 83
Programmable Array Logic (PAL)
INPUT
S
OUTPUTS

## Slide 84
Programmable Array Logic (PAL)
X(A,B,C)= ∑m(2,3,5,7)=
Y(A,B,C)= ∑m(0,1,5)=
Z(A,B,C)= ∑m(0, 2,3,5)=
A
B
C
X
Y
Z
Step 1 Make the truth table
Step2 Minimal SOP using k-map

## Slide 85
Programmable Array Logic (PAL)
X(A,B,C)= ∑m(2,3,5,7)=A’B+AC
Y(A,B,C)= ∑m(0,1,5)=A’B’+B’C
Z(A,B,C)= ∑m(0, 2,3,5)=A’B+A’C+AB’C
A
B
C
X
Y
Z

## Slide 86
Programmable Array Logic (PAL)
X(A,B,C)= ∑m(2,3,5,7)=A’B+AC
Y(A,B,C)= ∑m(0,1,5)=A’B’+B’C
Z(A,B,C)= ∑m(0, 2,3,5)=A’B+A’C+AB’C
A
B
C
X
Y
Z
A’B
AC
B’C
A’B’
A’C
X
AB’C
A’B

## Slide 87
Implement the following Boolean function with a PAL:
Y1(A,B,C)=∑m(4, 5,7)
Y2(A,B,C)=∑m(3, 5,7)
Programmable Array Logic (PAL)

## Slide 88
Implement the following Boolean function with a PAL:
Programmable Array Logic (PAL)
W = ABC+CD
X = ABC+ACD+ACD+BCD
Y = ACD+ACD+ABD
x
x
x
x

## Slide 89
Implement the following Boolean function with a PAL:
Programmable Array Logic (PAL)
W = ABC+CD
X = ABC+ACD+ACD+BCD
Y = ACD+ACD+ABD
x
x
x
x

## Slide 90: THANKS