## Slide 1: ICT 2103 Digital Logic Design
Prof. Dr. Muhammad Shahin Uddin
Email: shahin.uddin@mbstu.ac.bd

## Slide 2: Combinational Circuits
Output is function of input only
  i.e. no feedback
  When input changes, output may change (after a delay)
•
•
•
•
•
•
n inputs
m outputs
Combinational
Circuits


## Slide 3
Combinational Circuit Vs. Sequential Circuit
Combinational Circuit | Sequential Circuit
Output depends only upon present input | Output depends upon present as well as past input
Speed is fast. | Speed is slow.
It is designed easy. | It is designed tough as compared to combinational circuits.
There is no feedback between input and output. | There exists a feedback path between input and output.
This is time independent. | This is time dependent.
Elementary building blocks: Logic gates | Elementary building blocks: Flip-flops
Used for arithmetic as well as Boolean operations. | Mainly used for storing data.
Combinational circuits don’t have capability to store any state. | Sequential circuits have capability to store any state or to retain earlier state.
As combinational circuits don’t have clock, they don’t require triggering. | As sequential circuits are clock dependent they need triggering.
These circuits do not have any memory element. | These circuits have memory element.
It is easy to use and handle. | It is not easy to use and handle.
Examples: Encoder, Decoder, and Multiplexer, Demultiplexer | Examples: Flip-flops, and Counters

## Slide 4: Sequential Circuits
Combinational
Circuit
Memory Elements
Inputs
Outputs
Asynchronous
Synchronous
Combinational
Circuit
Flip-flops
Inputs
Outputs
Clock

## Slide 5
SR Latch :
NOR
NAND
Reset
Q=0
Set
=1
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Case 1:
1 0 0 0
0 0 1 0
0 0 1 1
1 1 0 0
S=0, R=1
Q= 0
=1
S=0, R=0
Q= 0
=1
Case 2:
No Change: (Memory )
S=1, R=0
Q= 1
=0
S=0, R=0
Q= 1
=0
No Change: Memory
Q’=1 0
Q=0
Case 3:
S=1, R=1 Q=0 Q’=0
Reset
Q=0
Set
=1
1
0
0
1
S=0, R=0 Q=0 Q’=0

## Slide 6: Latches
SR Latch
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
1 1 1 |  | 
1
0
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0
Q = Q’

## Slide 7: Latches
SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
C S R | Q
0 x x | Q0
1 0 0 | Q0
1 0 1 | 0
1 1 0 | 1
1 1 1 | Q=Q’
No change
No change
Reset
Set
Invalid
SR Latch with Control Input
S
Q
Q
R

## Slide 8: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
D
D
Q
Q
C

## Slide 9: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change
D
Q
Q
Q (t+1) = D
When Clock is enabled
Q(t+1) = Q(t)
When Clock is disabled
C

## Slide 10: Controlled Latches (Task 1)
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change
D
Q
Q
Q (t+1) = D
When Clock is enabled
Q(t+1) = Q(t)
When Clock is disabled

## Slide 11: Controlled Latches
D Latch (D = Data)
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
Output may change
D
Q
Q
Q (t+1) = D
When Clock is enabled
Q(t+1) = Q(t)
When Clock is disabled

## Slide 12: Flip-Flops
Controlled latches are level-triggered
Flip-Flops are edge-triggered
C
CLK
Positive Edge
CLK
Negative Edge
Q (t+1) = D
When Clock is enabled
Q(t+1) = Q(t)
When Clock is disabled

## Slide 13
S | R | Q | Q’
0 | 0 | NO change | 
0 | 1 | 0 | 
1 | 0 | 1 | 
1 | 1 | Not Used | 
High Falling Edge
High
High Falling Edge

## Slide 14: Flip-Flops
Master-Slave D Flip-Flop
D Latch
(Master)
D
C
Q
D Latch
(Slave)
D
C
Q
Q
D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave

## Slide 15: Flip-Flops
JK Flip-Flop
J
Q
Q
K
D = JQ’ + K’Q
Q (t+1) = D = JQ’ + K’Q
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)

## Slide 16: Flip-Flops
T Flip-Flop
D = TQ’ + T’Q = T  Q
J
Q
Q
K
T
D
Q
Q
T
D = JQ’ + K’Q
T
Q
Q

## Slide 17: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 18: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 19: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 
1 | 1 | 1 | 
No change
Reset
Set
Toggle

## Slide 20: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
No change
Reset
Set
Toggle

## Slide 21: Flip-Flop Characteristic Equations
Analysis / Derivation
J
Q
Q
K
J | K | Q(t) | Q(t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
 |  |  |  | K | 
 |  | 0 | 1 | 0 | 0
J |  | 1 | 1 | 0 | 1
 |  |  | Q |  | 
Q(t+1) = JQ’ + K’Q

## Slide 22: Flip-Flop Characteristic Tables
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset
Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change
Reset
Set
Toggle
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change
Toggle

## Slide 23: Flip-Flop Characteristic Equations
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T  Q

## Slide 24
SR and JK flip flop

## Slide 25
Race Around Condition of JK flip flop
1
0

## Slide 26
Conditions to overcome Racing :
T/2<Propagation delay of FF x
Edge Triggering
Master-Slave
Race Around Condition of JK flip flop
1
0

## Slide 27
JK flip flop Master Slave Operation of JK flip flop
Master
Slave
T/2<Propagation Delay of FF
Edge Triggered
Master-Slave (M.S. operation is same as negative edge triggering])
Qm

## Slide 28: Flip-Flop Characteristic Tables
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset
Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change
Reset
Set
Toggle
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change
Toggle

## Slide 29: Flip-Flop Characteristic Equations
D
Q
Q
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
J
Q
Q
K
T
Q
Q
Q(t+1) = TQ’+T’Q =T  Q
0 | 1 | 0 | 0
1 | 1 | 0 | 1
J
0
1
KQ
00 01 11 10
0 | 1
1 | 0
T
0
1
Q
0 1
0 | 0
1 | 1
D
0
1
Q
0 1
D | Q | Q(t+1)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
T | Q | Q(t+1)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 30: Clocked Sequential Circuits
Analyzing a clocked sequential circuit
Designing a sequential circuit to address a problem

## Slide 31: Analyzing a Clocked Sequential Circuit

## Slide 32
State Table and State Diagram
State Diagram
The state diagram is the pictorial representation of the behavior of sequential circuits. It clearly shows the transition of states from the present state to the next state and output for a corresponding input.
State table
The information contained in the state diagram is transformed into a table called as state table or state synthesis table. Although the state diagram describes the behavior of the sequential circuit, in order to implement it in the circuit, it has to be transformed into the tabular form.

## Slide 33: Analyzing a Clocked Sequential Circuit
A circuit will be given and we must understand the boundary between combinational stage and sequential stage
Then identify the following specifications
  No. flip flops and what types
  How many external input
  How many external output
  No. of state variable (n)
  No of states, 2n

## Slide 34: Analyzing a Clocked Sequential Circuit
Write down the equation of Flip Flop Input, External Output [3]
Write down the equation for flip-flop output (known as state equation). This can be written by combining [3] with the flip flop’s driving equation.
Draw the state table
Draw the state diagram

## Slide 35: Analyzing a Clocked Sequential Circuit

## Slide 36: Analyzing a Clocked Sequential Circuit

## Slide 37: Analyzing a Clocked Sequential Circuit: Next state and output Equations

## Slide 38: Analyzing a Clocked Sequential Circuit: State Table

## Slide 39: Analyzing a Clocked Sequential Circuit: State Diagram
v.v.i

## Slide 40: Analyzing a Clocked Sequential Circuit with T Flip-Flop

## Slide 41: Recall: Flip-flop Characteristic Equation

## Slide 42: Sequential Circuit with T Flip-flops

## Slide 43: Analyzing a Clocked Sequential Circuit : From Next State Equations to state table

## Slide 44: Sequential Circuit with JK FF
HW state diagram

## Slide 45: Analyzing a Clocked Sequential Circuit: JK Input and Next State Equations

## Slide 46: Analyzing a Clocked Sequential Circuit

## Slide 47: Analyzing a Clocked Sequential Circuit

## Slide 48
Design a Sequential Circuit

## Slide 49: Classifications of Counters
Asynchronous Counters
  Only the first flip-flop is clocked by an external clock. All subsequent flip-flops are clocked by the output of the preceding flip-flop.
  Asynchronous counters are slower than synchronous counters because of the delay in the transmission of the pulses from flip-flop to flip-flop.
  Asynchronous counters are also called ripple-counters because of the way the clock pulse ripples it way through the flip-flops.
Synchronous Counters
  All flip-flops are simultaneously clocked by an external clock.
  Synchronous counters are faster than asynchronous counters because of the simultaneous clocking.
  Synchronous counters are an example of a state machines design.

## Slide 50: Design Synchronous Counter

## Slide 51: Design Synchronous Counter
0 0
0 1
0
1 1

## Slide 52: Binary Counter Example
How about a random number generator.
Check the following state diagram and try to identify what it is trying to do :

## Slide 53: Binary Counter Example
How about a random number generator.
Check the following state diagram and try to identify what it is trying to do :

## Slide 54: Binary Counter Example
How about a random number generator.

## Slide 55
Binary Counter Example

## Slide 56
Binary Counter Example

## Slide 57: Counters: Ring counter
Ring counter: Sequence is 1000, 0100, 0010, 0001
  Assuming one of these patterns is the starting state
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 58: Counters: Johnson counter
Johnson counter: Sequence is 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 59: Counters: Ripple counter

## Slide 60
Build a 4 Bit Ripple Counter
1. 4 JK flip-flops in toggle mode- all JK inputs tied high
2. Q outputs connected to clock input of following flip-flop
3. FF A = LSB (one with clock input); toggles when input clock
toggles from high to low; FF D = MSB
4. FF B, C, D do not toggle till receive NGT from proceeding FF
5. Direction of count can be reversed by complementing each FF’s output or complementing each FF’s input

## Slide 61
Build A Counter that Count from Zero to Nine
1. Determine smallest number of FF’s such that
thus 4 FF’s are required
2. Connect a NAND gate to asynchronous clears of all FF’s
3. Determine which FF’s will be high at count = X
Connect the Q outputs of these FF’s to NAND gate inputs
1
1
0
0

## Slide 62
Self-stopping Counter
Counters may be made to stop counting after any desired count by using a gate to inhibit the clock.
Stop at desired count:
D
B
C
A

## Slide 64: Examples of Different Counter

## Slide 65: Counters: Ring counter
Ring counter: Sequence is 1000, 0100, 0010, 0001
  Assuming one of these patterns is the starting state
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 66: Counters: Johnson counter
Johnson counter: Sequence is 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK

## Slide 67: Counters: Ripple counter

## Slide 68
Build a 4 Bit Ripple Counter
1. 4 JK flip-flops in toggle mode- all JK inputs tied high
2. Q outputs connected to clock input of following flip-flop
3. FF A = LSB (one with clock input); toggles when input clock
toggles from high to low; FF D = MSB
4. FF B, C, D do not toggle till receive NGT from proceeding FF
5. Direction of count can be reversed by complementing each FF’s output or complementing each FF’s input

## Slide 69
Build A Counter that Count from Zero to Nine
1. Determine smallest number of FF’s such that
thus 4 FF’s are required
2. Connect a NAND gate to asynchronous clears of all FF’s
3. Determine which FF’s will be high at count = X
Connect the Q outputs of these FF’s to NAND gate inputs
1
1
0
0

## Slide 70
Self-stopping Counter
Counters may be made to stop counting after any desired count by using a gate to inhibit the clock.
Stop at desired count:
D
B
C
A

## Slide 72: Examples of Different Counter

## Slide 73: Counter Design: Design a synchronous counter with counting sequence 0,1,2,4,5,6 using J-K flip-flop.

## Slide 74
Traffic Signal Problem: Traffic Light Controller

## Slide 75
Traffic Signal Problem: Traffic Light Controller

## Slide 76: THANKS